# Static Code Checkers
Static program analysis is the analysis of computer software performed without executing any programs. Often the use of static code checkers is required in critical applications of different sort. Generally speaking the source code generated by sinelabore should create no or little issues. But some points should be considered (see below).
One of the well known tools in this category is PC-lint from Gimpel Soft (https://www.gimpel.com). Another free one is cppcheck. Generated C/C++ code is regularly tested with cppcheck and its misra checker. Details about cppcheck can be found here: https://cppcheck.sourceforge.io/manual.pdf
## C-Code
For C-code the following parameter settings are suggested in the codegen.cfg file:
#It is recommended to set the following parameters to include the standard types.
#Additional include in the validate h file to provide data types
AdditionalValidateIncludes=#include <stdint.h>\n#include <stdbool.h>
#
# Include file which can be used to define the simple data types
AdditionalMachineInclude=#include <stdint.h>\n#include <stdbool.h>
#Setting the used types to avoid problems with boolean comparisons ...
UINT8 = uint8_t
UINT16 = uint16_t
BOOL=bool
BOOL_TRUE=true
BOOL_FALSE=false
#Avoid issues about not used variable
ReturnEventProcessed=yes
UseUnderlineForIncludeProtection=no
## C++ Code
It is recommended to use the newer features of C++11.
#Avoid issues about not used variable
ReturnEventProcessed=yes
#Avoid issues of not initialised variables in the ctor
CallInitializeInCtor = yes
#This enables the uses of array ...
UseEnumBaseTypes = YES
EnumBaseTypeForEvents = std::uint16_t
EnumBaseTypeForStates = std::uint32_t
ReturnAndProcessEventTypeOfStateMachine = std::uint16_t
InitializedFlagTypeOfStateMachine = std::uint16_t
UseUnderlineForIncludeProtection=no